## Slide 1: Wireless and Mobile Networks
Wireless and 802.11 LANs
wireless links:
  shared, fading, interference, hidden terminal problem
IEEE 802.11 (“wi-fi”)
  CSMA/CA reflects wireless channel characteristics
  DIFS, SIFS, receiver ACK, RTS/CTS, NAV, …
Cellular Network Architectures (and its Evolution): an Overview
An overview of cellular network architecture
3G and 4G LTE cellular networks
Mobility
principles: addressing, routing to mobile users
  home, visited networks
  direct, indirect routing
  care-of-addresses
case studies
  mobile IP; mobility management in cellular networks
Readings: Textbook, Chapter 7

## Slide 2: Ch. 6: Wireless and Mobile Networks
Background:
# wireless (mobile) phone subscribers now exceeds # wired phone subscribers (5-to-1)!
# wireless Internet-connected devices equals # wireline Internet-connected devices
  laptops, Internet-enabled phones promise anytime untethered Internet access
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 3: Chapter 7 outline
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  CDMA
7.3 IEEE 802.11 wireless LANs (“wi-fi”)
7.4 Cellular Internet Access
  architecture
  standards (e.g., GSM)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols
7.9 Summary

## Slide 4: Elements of a Wireless Network
network
infrastructure
wireless hosts
laptop, PDA, IP phone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility

## Slide 5: Elements of a Wireless Network
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers 802.11 access points
network
infrastructure

## Slide 6: Elements of a Wireless Network
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access protocol coordinates link access
various data rates, transmission distance
network
infrastructure

## Slide 7: Characteristics of selected wireless links
Indoor
10-30m
Outdoor
50-200m
Mid-range outdoor
200m – 4 Km
Long-range outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
2G: IS-95, CDMA, GSM
2.5G: UMTS/WCDMA, CDMA2000
802.15
802.11b
802.11a,g
3G: UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
4G: LTWE WIMAX
802.11a,g point-to-point
450
802.11n
Data rate (Mbps)
1300
802.11 ac

## Slide 8: Wireless Link Characteristics (1)
Differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
  multipath propagation: radio signal reflects off objects ground, arriving ad destination at slightly different times
…. make communication across (even a point to point) wireless link much more “difficult”

## Slide 9: Wireless Link Characteristics (2)
SNR: signal-to-noise ratio
  larger SNR – easier to extract signal from noise (a “good thing”)
SNR versus BER tradeoffs
  given physical layer: increase power -> increase SNR->decrease BER
  given SNR: choose physical layer that meets BER requirement, giving highest thruput
    SNR may change with mobility: dynamically adapt physical layer (modulation technique, rate)
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4

## Slide 10: Wireless Network Characteristics
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 11: Optional: A Brief Intro to Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
encoded signal = (original data) X (chipping sequence)
decoding: inner-product of encoded signal and chipping sequence

## Slide 12: CDMA Encode/Decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
Di = S Zi,m.cm
m=1
M
M

## Slide 13: CDMA: Two-sender Interference
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions by sender 1 and 2

## Slide 14: Back to Wireless Networks: A Taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to
base station (WiFi,
WiMAX, cellular)
which connects to
larger Internet
no base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
no base station, no
connection to larger
Internet. May have to
relay to reach other
a given wireless node
MANET, VANET

## Slide 15: Elements of a Wireless Network
network
infrastructure
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network

## Slide 16: Elements of a Wireless Network
Ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 17: IEEE 802.11 Wireless LAN
802.11b
  2.4-5 GHz unlicensed radio spectrum
  up to 11 Mbps
  direct sequence spread spectrum (DSSS) in physical layer
    all hosts use same chipping code
  widely deployed, using base stations
802.11a
  5-6 GHz range
  up to 54 Mbps
802.11g
  2.4-5 GHz range
  up to 54 Mbps
802.11n
  MIMO, 20/40MHz channels in 2.4 GHz
  up to 600 Mbps
802.11ac
  wider RF band per station (80/160 MHz), more MIMO, multi-user MIMO, 5 GHz
  at least 1 Gbps total, 500 Mbps per link
All use CSMA/CA for multiple access
All have base-station and ad-hoc network versions

## Slide 18: 802.11 LAN Infrastructure Mode
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
hub, switch
or router
AP
AP

## Slide 19: 802.11: Channels, Association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  may perform authentication [Chapter 8]
  will typically run DHCP to get IP address in AP’s subnet

## Slide 20: 802.11: Passive/Active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 21: Ad Hoc Network Approach
No access point (i.e., base station)
  “peer-to-peer” mode
wireless hosts communicate with each other
  to get packet from wireless host A to B may need to route through wireless hosts X,Y,Z
Applications:
  “laptop” meeting in conference room, car
  interconnection of “personal” devices
  battlefield
IETF MANET (Mobile Ad hoc Networks) working group

## Slide 22: Wireless Network Characteristics (again!)
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other
means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal fading:
B, A hear each other
B, C hear each other
A, C can not hear each other interferring at B

## Slide 23: Hidden and Exposed Terminal Problems
Wireless networks: hidden and exposed nodes
  A->B and C->B: A can’t hear C’s transmission
    C hidden from A, can cause collision!
  B->A and C->D: won’t interfere with each other, despite B can hear C’s transmission
    C exposed to B,
    unnecessary backoff by B!

## Slide 24: IEEE 802.11: Multiple Access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading);
    often need to switch between transmitting vs. receiving mode
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/C(ollision)A(voidance)
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 25: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff timer
  timer counts down while channel idle
  transmit when timer expires
if no ACK (e.g., due to collision or bit error), increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK

## Slide 26: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff timer
  timer counts down while channel idle
  transmit when timer expires
if no ACK (e.g., due to collision or bit error), increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK
Key Design decisions/questions:
a) why DIFS & SIFS intervals?
b) why requiring ACK?
c) why DIFS > SIFS?
What issues we may still have?
What can we do better?

## Slide 27: IEEE 802.11 MAC Protocol: CSMA/CA
sender
receiver
DIFS
data
SIFS
ACK
Key Design decisions/questions:
a) why DIFS & SIFS intervals?
b) why requiring ACK?
c) why DIFS > SIFS?
What issues we may still have?
What can we do better?

## Slide 28: Collision Avoidance Mechanisms
Problem:
  two nodes, hidden from each other, transmit complete frames to base station
  wasted bandwidth for long duration !
Solution:
  small reservation packets
  nodes track reservation interval with internal “network allocation vector” (NAV)

## Slide 29: Avoiding Collisions (cont’d)
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
RTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
Avoid (large) data frame collisions
using small reservation packets!

## Slide 30: Collision Avoidance: Some Details
Sender transmits RequestToSend (RTS) frame
Receiver replies with ClearToSend (CTS) frame
Neighbors…
  see CTS: keep quiet
  see RTS but not CTS: ok to transmit
Receiver sends ACK when has frame
  neighbors silent until see ACK
Collisions
  no collisions detection
  known when don’t receive CTS
  exponential backoff

## Slide 31: Collision Avoidance: RTS-CTS Exchange
sender transmits short RTS (request to send) packet: indicates duration of transmission
receiver replies with short CTS (clear to send) packet
  notifying (possibly hidden) nodes
hidden nodes will not transmit for specified duration: NAV

## Slide 32: Collision Avoidance: RTS-CTS Exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 33: 802.11 Frame: Addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address of original (i.e., actual!) source or target (i.e., actual) destination when frames are forwarded by AP
Address 4: used when frames are forwarded from one AP to another AP (MAC address of actual source)

## Slide 34
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
802.11 Frame: More
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for reliable ARQ)
frame type
(RTS, CTS, ACK, data)

## Slide 35
Internet
router
AP
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame
802.11 Frame: Addressing
To-AP=1; From-AP=0;
Not AP’s MAC address!
IP datagram
from H1 to W
W’s IP
addr
H1’s IP
addr
src IP addr
dst IP addr
802.11 Frame: Addressing
W
src & dst IP addresses in IP datagram are never altered on its journey from H1 to W!

## Slide 36
Internet
router
AP
H1
R1
H1 MAC addr AP MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
H1 MAC addr R1 MAC addr
dest. address
source address
802.3 frame
802.11 Frame: Addressing
To-AP=0; From-AP=1;
W
IP datagram
from W to H1
H1’s IP
addr
W’s IP
addr
src IP addr
dst IP addr
src & dst IP addr’s in IP datagram is never changed on its journey from W to H!

## Slide 37
AP1
A
AP1 MAC addr A MAC addr B MAC addr
address 1
address 2
address 3
802.11 frame
802.11 Frame: Use of Address 4
To-AP=1; From-AP=0;
AP2
B
address 4
NULL
mobile host A on AP1 sends an IP datagram to mobile host B on AP2
AP1 & AP2 are connected wireless
as a “wireless mess” network
from A to AP1 using WiFi 802.11

## Slide 38
AP1
A
AP2 MAC addr AP1 MAC addr B MAC addr
address 1
address 2
address 3
802.11 frame
802.11 Frame: Use of Address 4
To-AP=1; From-AP=1;
AP2
B
address 4
A’s MAC addr
mobile host A on AP1 sends an IP datagram to mobile host B on AP2
AP1 & AP2 are connected wireless
as a “wireless mess” network
From AP1 to AP2 using WiFi 802.11

## Slide 39
AP1
A
B MAC addr AP2 MAC addr A MAC addr
address 1
address 2
address 3
802.11 frame
802.11 Frame: Use of Address 4
To-AP=0; From-AP=1;
AP2
B
address 4
NULL
mobile host A on AP1 sends an IP datagram to mobile host B on AP2
AP1 & AP2 are connected wireless
as a “wireless mess” network
from AP2 to B using WiFi 802.11

## Slide 40
router
AP1
A
R
Exercise for You!
AP2
What about A sending an IP datagram to a web server W on the Internet?
Please work out the addresses in the 802.11/802.3 frame step-by-step from A to AP1, via AP2, then via switch S, finally to router R, as well as the reply from W to A from router R to host A via, S, AP2 and AP1!
Ethernet
switch
S
B
Internet
W
AP1 & AP2 are connected wireless
as a 802.11 “wireless mess” network
802.3 Ethernet link

## Slide 41
hub or
switch
AP 2
AP 1
H1
BBS 2
BBS 1
802.11: Mobility within Same Subnet
router
H1 remains in same IP subnet: IP address can remain same
switch: which AP is associated with H1?
  self-learning (Ch. 6): switch will see frame from H1 and “remember” which switch port can be used to reach H1

## Slide 42: Mobility with a Subnet(cont’d)
Scanning (selecting an AP)
  node sends Probe frame
  all AP’s w/in reach reply with ProbeResponse frame
  node selects one AP; sends it AssociateRequest frame
  AP replies with AssociationResponse frame
  new AP informs old AP via tethered network
When
  active: when join or move
  passive: AP periodically sends Beacon frame

## Slide 43
802.11: Advanced Capabilities
Rate adaptation
base station, mobile dynamically change transmission rate (physical layer modulation technique) as mobile moves, SNR varies
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
10
20
30
40
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
operating point
1. SNR decreases, BER increase as node moves away from base station
2. When BER becomes too high, switch to lower transmission rate but with lower BER

## Slide 44
power management
node-to-AP: “I am going to sleep until next beacon frame”
  AP knows not to transmit frames to this node
  node wakes up before next beacon frame
beacon frame: contains list of mobiles with AP-to-mobile frames waiting to be sent
  node will stay awake if AP-to-mobile frames to be sent; otherwise sleep again until next beacon frame
802.11: Advanced Capabilities

## Slide 45: A Word about Bluetooth
Low-power, small radius, wireless networking technology
  10-100 meters
omnidirectional
  not line-of-sight infrared
Interconnects gadgets
2.4-2.5 GHz unlicensed radio band
up to 721 kbps
Interference from wireless LANs, digital cordless phones, microwave ovens:
  frequency hopping helps
MAC protocol supports:
  error correction
  ARQ
Each node has a 12-bit address

## Slide 46
M
radius of
coverage
S
S
S
P
P
P
P
M
S
Master device
Slave device
Parked device (inactive)
P
802.15: Personal Area Network
less than 10 m diameter
replacement for cables (mouse, keyboard, headphones)
ad hoc: no infrastructure
master/slaves:
  slaves request permission to send (to master)
  master grants requests
802.15: evolved from Bluetooth specification
  2.4-2.5 GHz radio band
  up to 721 kbps

## Slide 47: Cellular Network Architectures: A Primer
Basics of Cellular Networks
Survey of 2G/3G Cellular Network Standards
  2G
  2.5G
  3G
  3.5G
  2.5G/3G Voice/Data Network Architectures
4G LTE/LTE Advanced Network Architectures

## Slide 48
Mobile
Switching
Center
Public telephone
network, and
Internet
Mobile
Switching
Center
connects cells to wide area net
manages call setup
handles mobility
MSC
covers geographical region
base station (BS) analogous to 802.11 AP
mobile users attach to network through BS
air-interface: physical and link layer protocol between mobile and BS
cell
wired network
Cellular Network Architecture: basic terminology & components

## Slide 49: Cellular networks: the first hop
Two basic techniques for sharing mobile-to-BS radio spectrum
combined FDMA/TDMA: divide spectrum in frequency channels, divide each channel into time slots
CDMA: code division multiple access
4G LTE also uses:
OFDM (orthogonal FDM)
frequency
bands
time slots

## Slide 50: Cellular Standards: Brief Survey
1G systems: analog voice systems; no standards
2G systems: digital voice channels
  IS-136 TDMA: combined FDMA/TDMA (North America)
  GSM (global system for mobile communications): combined FDMA/TDMA
    started by Europeans, most widely deployed in the world
  IS-95 CDMA: code division multiple access
2.5G: packet switched data channels “bolted-on” 2G
  General Packet Radio Service (GPRS)
    evolved from GSM, multiple data channels, up to 80 Kbps
  Enhanced data rates for global evolution (EDGE)
    also evolved from GSM, data rates up to 236.8K
  CDMA-2000 (phase 1)
    evolved from IS-95; data rates up to 144K

## Slide 51: Cellular Standards: Brief Survey
3G systems: supporting both voice/data
  Universal Mobile Telecommunications Service (UMTS)
    new spectrum and air interfaces, wideband CDMA (W-CDMA)
    achieve higher data rates; up to from 384Kbps to 7.2 Mbps
    both circuited switched and packet switched
  CDMA-2000 (1xRTT): CDMA in TDMA slots
    1xEvolution Data Optimized (1xEVDO): up to 14 Mbps
3.5G systems: evolved from 3G UMTS
  High Speed Packet Access (HSPA)
    includes High Speed Downlink/Uplink Packet Access (HS[D/U]PA)
  Evolved HSPA (HSPA+)
    data rates theoretically up to 84 Mbps or more
IS-136
GSM
IS-95
GPRS
EDGE
CDMA-2000
UMTS
TDMA/FDMA
Don’t drown in a bowl
of alphabet soup: use this
for reference only

## Slide 52
Base transceiver station (BTS)
Base station controller (BSC)
Mobile Switching Center (MSC)
Mobile subscribers
Base station system (BSS)
BSC
BTS
Legend
MSC
Public
telephone
network
Gateway
MSC
G
2G Voice Network Architecture
MSC
BSC
BTS
VLR
HLR
VLR
HLR
VLR
home/visitor location registers
SS7 control network
AuC
authen. center
BSC
BSC

## Slide 53
BSC
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Public
Internet
BTS
GGSN
G
Serving GPRS
Support Node (SGSN)
Gateway GPRS
Support Node (GGSN)
Radio network controller
RNC
RNC
NodeB
GPRS & UMTS Network Architectures
Voice
Data
Core Network
Radio Access Networks (RANs)
3G UTRAN
2.5G GERAN

## Slide 54
3G (voice+data) Network Architecture
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Serving GPRS Support Node (SGSN)
Gateway GPRS Support Node (GGSN)
Public
Internet
GGSN
G
Key insight: new cellular data
network operates in parallel
(except at edge) with existing
cellular voice network
voice network unchanged in core
data network operates in parallel

## Slide 55
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Public
Internet
GGSN
G
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
core network
General Packet Radio Service
(GPRS) Core Network
public
Internet
radio interface
(WCDMA, HSPA)
3G (voice+data) Network Architecture

## Slide 56: 4G LTE/LTE Advanced
LTE: Long Term Evolution (3GPP Release 8 &9)
  likely the first global cellular network architecture standard
  although many network operators may use different bands
fully packet-switched, all IP-based
  optimized for data services, up to 1 Gpbs
  new packet-switched air interfaces, reducing latency, use OFDM, MIMO, …
  Support cell sizes varying from 10s m (femto or pico cells) up to 100 km/62 miles (macro cells)
  simplified radio access networks (e-UTRANs) and packet switched core network (SAE -- System Arch. Evolution)
  support for inter-operation and co-existence with (all) legacy systems (e.g., GSM, UMTS, CDMA200)

## Slide 57
MSC
Public
telephone
network
Gateway
MSC
G
Mobility Management Entity(MME)
4G LTE Network Architecture
Legacy 2G/3G
Cellular Voice
evolved Packet Core Network
Radio Access Networks (RANs)
SGW/MME
Public
Internet
PGW
G
eNodeB
4G eUTRAN
HSS
RNC
NodeB
All-IP
Serving Gateway (SGW)
PDN Gateway (PGW)
Home Subscriber Server (HSS)
User Equipment (UE)

## Slide 58
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Public
Internet
G
3G vs. 4G LTE Network Architecture
GGSN
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
Evolved Packet Core
(EPC)
MME
Public
Internet
P-GW
G
S-GW
G
HSS
3G
4G-LTE

## Slide 59
4G: Differences from 3G
all IP core: IP packets tunneled (through core IP network) from base station to gateway
no separation between voice and data – all traffic carried over IP core to gateway
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
Evolved Packet Core
(EPC)
Public
Internet
P-GW
G
S-GW
G
UE
(user element)
eNodeB
(base station)
Packet data
network
Gateway
(P-GW)
Serving
Gateway
(S-GW)
data
MME
HSS
Mobility
Management
Entity (MME)
control
Home Subscriber
Server(HSS)
(like HLR+VLR)

## Slide 60
Functional split of major LTE components
holds idle UE info
QoS enforcement
handles idle/active UE transitions
pages UE
sets up eNodeB-PGW tunnel (aka bearer)

## Slide 61
Radio+Tunneling: UE – eNodeB – PGW
tunnel
link-layer radio net
UE
eNodeB
S-GW
G
P-GW
G
IP packet from UE encapsulated in GPRS Tunneling Protocol (GTP) message at ENodeB
GTP message encapsulated in UDP, then encapsulated in IP. large IP packet addressed to SGW
55
CSci4211 802.11 Wireless and Mobile Networks

## Slide 62
Quality of Service in LTE
QoS from eNodeB to SGW: min and max guaranteed bit rate
QoS in radio access network: one of 12 QCI values

## Slide 63: (Wide-Area) Mobility (optional)
What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
mobile wireless user,
using same access
point
mobile user, passing through multiple access point while maintaining ongoing connections (like cell phone)
mobile user, connecting/ disconnecting from network using DHCP.

## Slide 64: Mobility: Vocabulary
home network: permanent “home” of mobile
(e.g., 128.119.40/24)
Permanent address: address in home network, can always be used to reach mobile
e.g., 128.119.40.186
home agent: entity that will perform mobility functions on behalf of mobile, when mobile is remote
wide area network
correspondent

## Slide 65: Mobility: More Vocabulary
Care-of-address: address in visited network.
(e.g., 79,129.13.2)
wide area network
visited network: network in which mobile currently resides (e.g., 79.129.13/24)
Permanent address: remains constant (e.g., 128.119.40.186)
foreign agent: entity in visited network that performs mobility functions on behalf of mobile.
correspondent: wants to communicate with mobile

## Slide 66: How do you contact a mobile friend:
search all phone books?
call her parents?
expect her to let you know where he/she is?
I wonder where Alice moved to?
Consider friend frequently changing addresses, how do you find her?

## Slide 67: Mobility: Approaches
Let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
Let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile

## Slide 68: Mobility: Approaches
Let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile
not
scalable
to millions of
mobiles

## Slide 69: Mobility: Registration
End result:
Foreign agent knows about mobile
Home agent knows location of mobile
wide area network
home network
visited network
1
mobile contacts foreign agent on entering visited network
2
foreign agent contacts home agent home: “this mobile is resident in my network”

## Slide 70: Mobility via Indirect Routing
wide area network
home
network
visited
network
3
2
4
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 71: Indirect Routing: Comments
Mobile uses two addresses:
  permanent address: used by correspondent (hence mobile location is transparent to correspondent)
  care-of-address: used by home agent to forward datagrams to mobile
foreign agent functions may be done by mobile itself
triangle routing: correspondent-home-network-mobile
  inefficient when
  correspondent, mobile
  are in same network

## Slide 72: Indirect Routing: Moving between Networks
suppose mobile user moves to another network
  registers with new foreign agent
  new foreign agent registers with home agent
  home agent update care-of-address for mobile
  packets continue to be forwarded to mobile (but with new care-of-address)
mobility, changing foreign networks transparent: on going connections can be maintained!

## Slide 73: Mobility via Direct Routing
wide area network
home
network
visited
network
4
2
4
1
correspondent requests, receives foreign address of mobile
correspondent forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent
3

## Slide 74: Mobility via Direct Routing: Comments
overcome triangle routing problem
non-transparent to correspondent: correspondent must get care-of-address from home agent
  what if mobile changes visited network?

## Slide 75: Accommodating Mobility w/ Direct Routing
wide area network
1
foreign net visited
at session start
anchor
foreign
agent
2
4
new foreign
agent
3
5
correspondent
agent
correspondent
new
foreign
network
anchor foreign agent: FA in first visited network
data always routed first to anchor FA
when mobile moves: new FA arranges to have data forwarded from old FA (chaining)

## Slide 76: Mobile IP
RFC 3220
has many features we’ve seen:
  home agents, foreign agents, foreign-agent registration, care-of-addresses, encapsulation (packet-within-a-packet)
three components to standard:
  indirect routing of datagrams
  agent discovery
  registration with home agent

## Slide 77: Mobile IP: Indirect Routing
Permanent address: 128.119.40.186
Care-of address: 79.129.13.2
dest: 128.119.40.186
packet sent by correspondent
dest: 79.129.13.2
dest: 128.119.40.186
packet sent by home agent to foreign agent: a packet within a packet
dest: 128.119.40.186
foreign-agent-to-mobile packet

## Slide 78: Mobile IP: Agent Discovery
agent advertisement: foreign/home agents advertise service by broadcasting ICMP messages (typefield = 9)
R bit: registration required
H,F bits: home and/or foreign agent

## Slide 79: Mobile IP: Registration Example

## Slide 80
Components of Cellular Network Architecture
correspondent
MSC
MSC
MSC
MSC
MSC
wired public telephone
network
different cellular networks,
operated by different providers
recall:

## Slide 81: Handling mobility in Cellular Networks
home network: network of cellular provider you subscribe to (e.g., Sprint PCS, Verizon)
  home location register (HLR): database in home network containing permanent cell phone #, profile information (services, preferences, billing), information about current location (could be in another network)
visited network: network in which mobile currently resides
  visitor location register (VLR): database with entry for each user currently in network
  could be home network

## Slide 82
Public switched
telephone
network
mobile
user
home
Mobile
Switching
Center
HLR
home
network
visited
network
correspondent
Mobile
Switching
Center
VLR
GSM: Indirect Routing to Mobile
1
call routed
to home network
2
home MSC consults HLR,
gets roaming number of
mobile in visited network
3
home MSC sets up 2nd leg of call
to MSC in visited network
4
MSC in visited network completes
call through base station to mobile

## Slide 83
Mobile
Switching
Center
VLR
old BSS
new BSS
old
routing
new
routing
GSM: Handoff with Common MSC
handoff goal: route call via new base station (without interruption)
reasons for handoff:
  stronger signal to/from new BSS (continuing connectivity, less battery drain)
  load balance: free up channel in current BSS
  GSM doesn't mandate why to perform handoff (policy), only how (mechanism)
handoff initiated by old BSS

## Slide 84
Mobile
Switching
Center
VLR
old BSS
1
3
2
4
5
6
7
8
new BSS
1. old BSS informs MSC of impending handoff, provides list of 1+ new BSSs
2. MSC sets up path (allocates resources) to new BSS
3. new BSS allocates radio channel for use by mobile
4. new BSS signals MSC, old BSS: ready
5. old BSS tells mobile: perform handoff to new BSS
6. mobile, new BSS signal to activate new channel
7. mobile signals via new BSS to MSC: handoff complete. MSC reroutes call
8 MSC-old-BSS resources released
GSM: Handoff with Common MSC

## Slide 85
home network
Home MSC
PSTN
correspondent
MSC
anchor MSC
MSC
MSC
(a) before handoff
GSM: Handoff between MSCs
anchor MSC: first MSC visited during call
  call remains routed through anchor MSC
new MSCs add on to end of MSC chain as mobile moves to new MSC
optional path minimization step to shorten multi-MSC chain

## Slide 86
home network
Home MSC
PSTN
correspondent
MSC
anchor MSC
MSC
(b) after handoff
anchor MSC: first MSC visited during call
  call remains routed through anchor MSC
new MSCs add on to end of MSC chain as mobile moves to new MSC
optional path minimization step to shorten multi-MSC chain
GSM: Handoff between MSCs
MSC

## Slide 87
Handling Mobility in LTE
Paging: idle UE may move from cell to cell: network does not know where the idle UE is resident
  paging message from MME broadcast by all eNodeB to locate UE
Handoff: similar to 3G:
  preparation phase
  execution phase
  completion phase
P-GW
old
eNodeB
old
routing
new
routing
new
eNodeB
source
MME
target
MME

## Slide 88: Mobility: Cellular versus Mobile IP
cellular element |  | Comment on cellular element | Mobile IP element | 
Home system | Network to which mobile user’s permanent phone number belongs |  |  | Home network
Gateway Mobile Switching Center, or “home MSC”. Home Location Register (HLR) | Home MSC: point of contact to obtain routable address of mobile user. HLR: database in home system containing permanent phone number, profile information, current location of mobile user, subscription information |  |  | Home agent
Visited System | Network other than home system where mobile user is currently residing |  |  | Visited network
Visited Mobile services Switching Center. Visitor Location Record (VLR) | Visited MSC: responsible for setting up calls to/from mobile nodes in cells associated with MSC. VLR: temporary database entry in visited system, containing subscription information for each visiting mobile user |  |  | Foreign agent
Mobile Station Roaming Number (MSRN), or “roaming number” | Routable address for telephone call segment between home MSC and visited MSC, visible to neither the mobile nor the correspondent. |  |  | Care-of-address

## Slide 89: Wireless, Mobility: Impact on Higher Layer Protocols
logically, impact should be minimal …
  best effort service model remains unchanged
  TCP and UDP can (and do) run over wireless, mobile
… but performance-wise:
  packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handoff
  TCP interprets loss as congestion, will decrease congestion window un-necessarily
  delay impairments for real-time traffic
  limited bandwidth of wireless links

## Slide 90: Wireless and Mobile Networks Summary
Wireless
wireless links:
  capacity, distance
  channel impairments
  CDMA
IEEE 802.11 (“Wi-Fi”)
  CSMA/CA reflects wireless channel characteristics
cellular access
  architecture
  standards (e.g., 3G, 4G LTE)
Mobility
principles: addressing, routing to mobile users
  home, visited networks
  direct, indirect routing
  care-of-addresses
case studies
  mobile IP
  mobility in GSM, LTE
impact on higher-layer protocols